## Slide 1: Low Power Jamming Mitigation PDR
Presented: 12/14/18
Senior Design I
By: Bryce Reese, Gary Visser, Alex English, Eric Routhier

## Slide 2: Problem
Jamming of radio frequency signals has been a problem since the advancement of technology during World War II
Jamming today, while technically illegal, is a huge issue as the technology to jam signals is easily obtainable for a small cost
The problem of Radio Frequency jamming can affect consumers, Governments, Militaries, and companies for signals big and small
Wireless mobile networks are easily disrupted by low power transmissions, making information loss a major risk

## Slide 3: Our Project Proposal
Design a countermeasure system for a multi-nodal wireless network that combines various detection, localization, and mitigation methods techniques derived from research and testing
A base station (laptop) will monitor received signal strength (RSS) from all nodes to calculate a known distance, in the event of a jamming attack, RSS will increase significantly, alerting the system. Nodes will be classified into three categories based on the location of the attack:
  Jammed: Node currently being attacked, information lost
  Barrier: Node is adjacent to a jammed node, transmission is secure for now
  Unharmed: Node is not adjacent to a jammed node, transmission is safe
Network channel will be switched by base station for all unaffected nodes, jammed nodes will follow suit via psuedo-random sequence.

## Slide 4: Justification
Jamming is an issue for not only the military, but for big companies and the general public as well
Jammed military comms can cost soldiers their lives or make missions into failures
Illegally purchased jammers can be very dangerous near airports
Oversaturated Wi-Fi and Bluetooth can lead to a very weak signal

## Slide 5
Diagram of Ideal System

## Slide 6
Diagram of Constrained System

## Slide 7: Multiple Solutions
Design a multi-nodal wireless network that is monitored indefinitely by a base station
  Low power signals make it easier to make without expensive equipment
Static System as opposed to mobile system
  Heritage, much more research and development, outside of scope of the project
  High power, UHF/VHF communication, testing will be difficult to obtain permits for in the region
Using Node redirection a signal can be redirected around an isolated jammer.
  Requires equipment including more Tx/Rx systems that are out of the foreseeable budget.
Random Frequency hopping in strings of packets that are decoded on the Base Station.
  Requires equipment including wideband arrays that are out of the foreseeable budget.

## Slide 8: Requirement Specifications
Physical: standard node may be small and safely stored from interference
Software needs to operate with the node system and frequency hopping and also be able to detect and localizing the jammer (GNU, Python, Raspian)
Outputs:
  Low power radio waves
  Jamming radio waves
  Report alerts on jamming, status of nodes. (clear, not clear, frequency level for transmitting)

## Slide 9: Requirement Specifications (Performance)
Be able to transmit reliably across a distance regardless of jamming
It must be able to quickly detect jamming in less than a minute
It can transmit on both frequency ranges (2.4, 2.45 or even 2.5 GHz)
Needs to run off low power, from a battery supply or extension cord

## Slide 10: Requirement Specifications (Testing)
Nees to be able to operate in an open air environment
  10 to 15 yard field test
  Test will be in a location free from many stray radio waves around area
Must abide by FCC regulation
  High level Jamming is illegal in the USA

## Slide 11: Assumptions and Constraints
Assumptions
  Materials
    3-4 Micro-computers (Raspberry Pis)
    Base station (Laptop)
    Power source
  Technology
    Coding language to work with Micro-computers (Python for Pis)
    Software to run the tests (GNURadio)
    Virtual machine to run the software
  Financial
    Between 4 group members, very limited budget
  Logistical
    Testing must be done in rural area
    Group messaging should be available for team

## Slide 12: Assumptions and Constraints Cont.
Constraints
  Limitations of project manager
    Need to find a mentor that has understanding of CE, AE, and EE.
  Anticipated barriers to completion
    FCC regulations (will need to verify the use of low energy jamming for educational use)
    Conditions necessary to create and maintain a private broadcast
    Funds are tight so project may need to be scaled down
  Anticipated barriers to large scale implementation
    Budget
      Implementation requires up to 7-8 nodes
    Size
      Scaled down project to match budget
        May cause problems while transmitting
  Generalizability of project findings
    With project being small scale, certain factors may need to be isolated

## Slide 13: Project Budget and Support
No Restrictions (appx. $390)
  5 nodes (Tx/Rx Capable): Raspberry Pi 3 ($90) Two supplied by Fusion Lab
  Stronger Bluetooth Emitters ($100)
  Power supply: MoPi ($40 ea. Or $120 for 3)
  Ground station: Simple computer, LINUX compatibility ($80)
  Software: Open-source code ($0)
Limited(appx. $30)
  3 nodes (Tx/Rx Capable): Raspberry Pi 3 ($30) Two being supplied by fusion lab
  Power supply (x3): EE Lab equipment ($0 if all components are available)
  Ground Station (laptop): Personal laptop fitted with Linux and software ($0)
  Software: Open source development ($0).

## Slide 14: Initial Project Schedule

## Slide 15: Literature Review
K. Grover, A. Lim, and Q. Yang. "Jamming and Anti-jamming Techniques in Wireless Networks: A Survey", International Journal of Ad Hoc and Ubiquitous Computing, vol. 17, no. 4, pp 197-215, 2014. Retrieved from https://www.cs.montana.edu/yang/paper/jamming.pdf
P. Rupani, N. Tada. “Literature Survey on Jamming Attack in Wireless Adhoc Network”, International Journal of Engineering Development and Research, vol. 5, no. 2, pp 434-443, 2017. Retrieved from https://www.ijedr.org/papers/IJEDR1702075.pdf
N. Sufyan, N. Saqib, & M. Zia. (2013, August 15). “Detection of jamming attacks in 802.11b wireless networks”, EURASIP Journal on Wireless Communications and Networking (n.p.). Retrieved from https://www.springer.com/engineering/signals/journal/13638
Huffman, M. (2012, March 2). The Effects of cognitive jamming on wireless sensor networks used for geolocation. Air Force Institute of Technology [University]. Retrieved from http://www.dtic.mil/dtic/tr/fulltext/u2/a557486.pdf
Pardhasaradhi, A., Kumar R. (2013, April). “Signal Jamming and its Modern Applications”, International Journal of Science and Research, vol. 2, iss. 4, pp 429-431, 2013. Retrieved from https://www.ijsr.net/archive/v2i4/IJSRON2013808.pdf

## Slide 16: Low Power Jamming Mitigation PDR
Questions?